## Slide 1: Solar IoT Digital Twin with an ANN + ANFIS Brain
Renewable-aware task offloading: should the device compute LOCAL or OFFLOAD to the edge?
Solar
Battery
ESP32
WiFi
Edge
Rohith Sivakumar
Notes: This project builds a digital twin of a solar-powered IoT device and an intelligent controller that decides, every minute, whether to process a task on the device or send it to an edge server.

## Slide 2: Every minute: LOCAL or OFFLOAD?
LOCAL
Run the task on the ESP32 itself
+ No WiFi needed, no waiting
− Slow for heavy tasks; CPU drains the battery
OFFLOAD
Send the data over WiFi to the edge server
+ Server is about 12× faster
− Radio costs energy; weak signal and busy server add delay
The best choice keeps changing with battery level, WiFi signal, server load and task size.
Notes: Analogy: doing homework yourself versus phoning a friend with a calculator. The call costs credit, a bad network means repeating, and the friend may be busy.

## Slide 3: Digital twin: a physics copy of the device
A software replica that follows the same physical equations as the real system, like a flight simulator for the IoT node. One step = one minute; 7 days = 10,080 tasks.
Solar PV
1 W panel, clouds & weather change daily
Battery
12 Wh Li-ion, SOC from energy balance
ESP32
240 MHz, computes local time & energy
WiFi / MQTT
RSSI → speed → packet errors → retries
Edge server
3 GHz, slower when busy (queue)
Notes: Each block is a sub-model with datasheet-level parameters. Randomness only comes from physical processes: clouds, shadowing, task arrivals and server traffic.

## Slide 4: What the twin does every simulated minute
1
Environment moves
Sun, clouds, distance to router, server traffic
2
Task arrives
Size (KB) × complexity (cycles/byte)
3
LOCAL costed
Time & energy on the ESP32
4
OFFLOAD costed
Upload + server + reply: time & radio energy
5
Cheaper bill wins
Compare cost J of both options
6
Battery updated
Chosen option's energy drained; loop repeats
Notes: This is a closed loop: the battery level after one minute is the starting point of the next, so every decision affects the future.

## Slide 5: Decision parameters and the cost "bill"
Battery SOC
low SOC → energy costs more (λ)
Task size × complexity
heavy task → favours OFFLOAD
WiFi signal (RSSI)
weak → retries → favours LOCAL
Server load
busy → long wait → favours LOCAL
Deadline 5 s
late answer → +2 penalty
Oracle cost (perfect knowledge)
λ = 1 + 4·(1 − SOC/100)^1.5
J_local = λ·E_loc + T_loc/5s
J_offload = λ·E_off + T_off/5s
+ 0.3·PER + 0.3·Load²
Smaller J wins → LOCAL / OFFLOAD
Low battery + good link → OFFLOAD saves energy. Low battery + weak link → stay LOCAL.
Notes: Lambda is the battery-risk price: 1 when full, 5 when empty. Solar only affects decisions through the battery. Missing the deadline adds +2 to either bill.

## Slide 6: The twin plays three roles
1 · Dataset
Simulates 7 days and records every minute: battery, task, signal, server load, costs.
10,080 rows × 38 columns
2 · Teacher (oracle)
Knows everything, so it gives the correct LOCAL / OFFLOAD answer for each minute.
the labels models learn from
3 · Test world
Trained controllers drive the twin's battery for a new, unseen week.
mistakes add up, like a real device
Notes: The twin is the world, the textbook and the exam. The ANN + ANFIS is the student. 20 automatic engineering checks confirm the twin behaves physically.

## Slide 7: Why a predictor is needed
The twin (oracle) knows
Exact upload time and packet errors
Exact radio energy
Current server load
→ perfect, but unrealistic
A real ESP32 only knows
Its battery level and the task
Its own local time & energy
Last measured WiFi signal
Last reported server load
Solution: an ANN predicts the unknown offload cost, and ANFIS turns it into a decision.
Notes: The oracle is like a student with the answer key: perfect, but not possible in a real exam. We use it only to teach and to grade.

## Slide 8: ANN predictor: the cost of offloading
Inputs (known)
Task size
Task complexity
Last WiFi signal
Last server load
Time of day
6 → 24 → 16 → 2 neurons
Outputs (predicted)
Offload time (ms)
Offload energy (mJ)
0.99
R² accuracy
~5 %
typical error
8,064
training minutes
Notes: The ANN learns like practising throws: guess, measure the mistake, adjust the weights (back-propagation and Adam), repeat. Trained on 80% of the data, checked on the last 20% it never saw. Example: predicted 180 ms, real 179 ms.

## Slide 9: ANFIS: learned fuzzy rules decide
ANN predicts
offload time + energy
Fuzzify 4 inputs
SOC · energy ratio · time gain · server
36 learned rules
score from 0 to 1
Decide
> 0.5 → OFFLOAD, else LOCAL
Real example: Day 1, 12:34 pm
FFT task, 105 KB · battery 27.6 % · server 69 % busy
ANN: offload ≈ 180 ms, 83.6 mJ (real 179 ms, 81 mJ)
Local: 385 ms, 46 mJ, so offload is faster but costs ~1.8× the energy
Strongest rule (50 %)
SOC Medium · Energy Similar · Time gain Small · Server Busy
→ LOCAL (score 0.16) ✓
Notes: ANFIS is fuzzy logic built like a neural network: it learns where words like Busy start and what each rule should output, from the oracle's answers. It is trained on the ANN's predictions, so it tolerates the ANN's errors. Every decision can be explained by the rule that fired. Here it matches the oracle: J_local 0.237 versus J_offload 0.483.

## Slide 10: Results on an unseen week
Chart: Ideal decisions matched (%)
| Fuzzy only | ANN only | ANN + ANFIS
Agreement with oracle (%) | 92.7 | 95.9 | 96.6
932 J
least task energy
−4.7 % vs fuzzy
9
deadline misses
vs 11 (ANN) and 16 (fuzzy)
Yes
explains every decision
the ANN alone cannot
Twin = world, teacher and exam · ANN = predicts the unknown · ANFIS = explainable decision
Notes: Each controller drove the battery itself for a new week it never saw. The hybrid came closest to the ideal decisions, used the least energy and missed the fewest deadlines, while still explaining every decision with readable rules.